## Slide 1: DIFFERENCE BETWEEN IPv4 AND IP v6
Both are major Internet Protocols which are used as the main communication protocol in the IP suite for transmitting information across the network

## Slide 2: IPv4 IPv6
Has address length of Has address length
32-bit of 128-bit
Represented in Represented in
Decimal format hexadecimal format
Supports manual and Supports Auto-
DHCP configuration configuration ,
renumbering,
manual and DHCP
configuration

## Slide 3: IPv4 IPv6
4.29 10^9 3.4 10^38
addresses can be addresses can be
generated generated
Security section is Has an inbuilt
dependant on security feature
application called Internet
Protocol Security

## Slide 4: IPv4 IPv6
Fragmentation is Fragmentation is
performed by both performed by
Sender and Forwarding Sender routers
routers
Authentication and Both authentication
Encription not provided and Encription are
provided

## Slide 5: IPv4 IPv6
The request header The request header
Is not fixed and is is fixed and is 40
20-60 bytes bytes only
No end-to-end Has end-to-end
encription integrity encription integrity
Checksum fields are Checksum fields are
Present absent

## Slide 6: IPv4 IPv6
Uses a broadcast Uses a multicasting
Information transfer information
mechanism technique hence
ensuring that
network services
are delivered
quickly